# PST Tool-Trial Questionnaire

| The tool will arrive at High Wycombe on |  | and will be available for | days. |
| --- | --- | --- | --- |
| Water fittings will be supplied with the tool including both male and female fittings as necessary. | Yes | No |
| If no, ensure the fittings are ordered and will arrive at HW on |  |  |
| The location ring is the correct diameter (see platen drawing) and will be supplied with the tool. | Yes | No |
| If no, ensure the correct location ring will be at HW on |  |  |

Tool Dimensions

| Will the tool fit between the tie bars? | Yes | width mm |
| --- | --- | --- |
| Is the mould height compatible with the machine? | Yes | height mm |
| Is the mould length (top to bottom) compatible? | Yes | length mm |
| Will the mould open fully enough to allow complete ejection of the part? | Yes |  |

Clamping

| How will the tool be attached to the platens? |
| --- |
| Will there be sufficient room on the platens for the fixings e.g. bolt holes, t-slots, platen area for clamps? |
| If bolts holes are required in the tool make sure they are the correct size and position for the platens. | Yes | N/A |
| Will the necessary fixings (ensure bolts are the correct thread size) be sent with the tool? | Yes | No |
| If no, ensure the fixings are ordered (e.g. mould clamps, t-bolts, bolts) and will arrive at HW on |  |

Nozzle

| The sprue bush radius is |  |
| --- | --- |
| If a special nozzle is required ensure all parts are ordered and will be at HW on |  |
| Will the nozzle reach the sprue bush when the tool is in situ? | Yes | No |
| If no, ensure an extended nozzle will arrive at HW on |  |  |
| Will the nozzle reach the sprue bush when the tool is in situ without fouling the tool platen or heaterbands? | Yes | No |
| If no, ensure the parts to rectify this will arrive at HW on |  |  |

Material

| Attach the material data sheet. |  |  |
| --- | --- | --- |
| Material type: |  |  |
| Shot weight: |  | grams |
| A sample of the moulding will arrive at HW on |  |  |
| The material needs drying for | hours at | (C |
|  | Kg’s of the material will arrive at HW on |  |

Tooling

| The tool needs to be controlled to a set temperature? | Yes | No |
| --- | --- | --- |
| If yes, the fixed half should be |  | (C and the moving half should be |  | (C |
| The ejector is tied to the tool via the standard ejector parts and stroke supplied on the machine? | Yes | No |
| If no, arrange any parts required for the ejector stroke, tie and/or knock off to be at HW on |  |
| Does the tool require hot tip control? | Yes | No |
| If yes, arrange for the controller and all cabling, thermocouples and heaterbands to be sent with the tool. This will arrive at HW on |  |
| Does the tool require core pull or unscrewing? | Yes | No |
| If yes, arrange for all cabling, switches and hoses to be sent with the tool. This will arrive at HW on |  |
| The sequence is |  |

Ancillaries

| Are any of the following required for the trial? | Quantity |  | Model / Type |
| --- | --- | --- | --- |
| Mould Heater | Yes No |  |  |  |
| Chiller | Yes No |  |  |  |
| Dryer | Yes No |  |  |  |
| Loader | Yes No |  |  |  |
| Doser | Yes No |  |  |  |
| Robot | Yes No |  |  |  |
| Granulator | Yes No |  |  |  |
| Ratio Mixer | Yes No |  |  |  |
| Conveyor | Yes No |  |  |  |

Please Save this file, then Email a copy to: sales@silicone-polymers.co.uk